## Slide 1
CASE STUDY
GHG Inventory &
Emissions Reporting
Tekstar Industries · Ahmedabad, India
Full Scope 1, 2 & 3 inventory built from raw activity data · GHG Protocol Corporate Standard
Conducted by
Praveen Gour
Sector
Textile Manufacturing
Reporting Year
2023
Standard
GHG Protocol Corporate
PG
Praveen Gour
Aspiring ESG & Sustainability Professional

## Slide 2
Praveen Gour | ESG Portfolio
Page 2
PROJECT OVERVIEW
Background & Objectives
Client Context
Tekstar Industries is a fictional mid-size textile manufacturer based in Ahmedabad, Gujarat — producing 8,020 tonnes of fabric annually, employing 750 staff and generating ₹2,500 Cr in revenue. The company exports to EU and US markets, making it subject to CSRD supply-chain disclosure requirements from its buyers.
Project Approach
Self-initiated end-to-end GHG inventory built from raw activity data — no pre-calculated figures used. Every tCO₂e value was derived independently through emission factor selection, calculation, scope aggregation and Power BI dashboard visualisation.
Objectives
Build complete GHG inventory — Scope 1, 2 & 3 — using GHG Protocol Corporate Standard
Apply appropriate EFs from CEA, DEFRA 2023 & IPCC; select location-based vs market-based for Scope 2
Calculate emission intensity ratios to benchmark operational performance
Identify highest-impact hotspots and translate into actionable reduction recommendations
Produce a Power BI dashboard for stakeholder communication

## Slide 3
Praveen Gour | ESG Portfolio
Page 4
GHG INVENTORY RESULTS
Total Emissions by Scope
Total Inventory
14,736
tCO₂e
Scope 1 — Direct
955
tCO₂e · 6.5%
Scope 2 — Energy
5,542
tCO₂e · 37.6%
Scope 3 — Value chain
8,238
tCO₂e · 55.9%
Chart: 
| Scope 1 (6.5%) | Scope 2 (37.6%) | Scope 3 (55.9%)
Emissions | 955 | 5542 | 8238
Emission Intensity
Intensity metric | Value
tCO₂e / tonne fabric output | 1.84
tCO₂e / ₹ Crore revenue | 5.89
tCO₂e / employee (FTE) | 19.6
Scope 2 grid EF used (location) | 0.82 kgCO₂e/kWh
Key Insight
Scope 3 dominates at 55.9% — consistent with textile sector benchmarks (40–60%). The biggest climate lever is product design for durability and recyclability, not just operational efficiency.

## Slide 4
Praveen Gour | ESG Portfolio
Page 5
GHG INVENTORY RESULTS
Scope 1 & Scope 2 Detail
Scope 1 — Key Sources (tCO₂e)
Chart: 
| Natural gas (boilers) | Diesel (genset+fleet) | N₂O (dyeing) | HFC (refrigerants) | LPG (canteen) | CH₄ (ETP) | Petrol (cars)
tCO₂e | 582 | 278 | 85 | 55 | 24 | 18 | 12
N₂O from dyeing carries 265× CO₂ GWP — disproportionate impact despite low physical mass. HFC-134a leaks (0.8–1.2 kg) = 1,430 GWP. Preventive maintenance is the lowest-cost Scope 1 lever.
Scope 2 — Electricity Breakdown
Meter / source | Annual kWh | tCO₂e
Main factory — Meter 1 | 3,826,000 | 3,137
Main factory — Meter 2 | 2,272,000 | 1,863
Purchased steam (CHP) | 530,000 kWh-th | 74
Admin block + Warehouse | 411,000 | 337
TOTAL | — | 5,542
Location vs Market-Based Method
Location-based
5,542 tCO₂e
CEA grid EF · 0.82 kgCO₂e/kWh
Market-based
5,542 tCO₂e*
*No RECs/PPAs held — equal to location-based
Switching to renewable electricity / RECs reduces Scope 2 to near-zero under market-based method — single highest-impact abatement lever available.

## Slide 5
Praveen Gour | ESG Portfolio
Page 6
GHG INVENTORY RESULTS
Scope 3 — Value Chain Breakdown
Chart: 
| Cat 11 · Consumer use (washing) | Cat 12 · Landfill disposal | Cat 12 · Incineration | Cat 4 · Road freight (inbound) | Cat 1 · Polyester procurement | Cat 1 · Cotton procurement | Cat 4 · Rail freight (inbound) | Cat 7 · Employee commute (bus) | Cat 7 · Commute (motorcycles) | Cat 9 · Export sea freight | Cat 7 · Commute (cars) | Cat 9 · Domestic road freight | Cat 1 · Chemical dyes | Other sources
tCO₂e | 3104 | 1063 | 570 | 508 | 464 | 384 | 347 | 320 | 322 | 271 | 238 | 236 | 198 | 213
F1
Cat 11 alone = 37.7% of Scope 3. Estimated via Higg Index LCA — lower confidence; actual value depends on consumer market energy mix.
F2
Cat 1 purchased goods (cotton + polyester + dyes) = 16% of Scope 3. Spend-based estimation — supplier primary data would improve quality.
F3
Upstream transport (Cat 4 road + rail) = 10.4% of Scope 3. Road EF is 2.2× rail — modal shift is a quick, measurable win.

## Slide 6
Praveen Gour | ESG Portfolio
Page 7
ANALYST COMMENTARY
Key Findings
01
Scope 3 Dominance
Scope 3 = 55.9% of total inventory — consistent with textile sector benchmarks (40–60%). Tekstar's biggest climate lever is product design for durability and recyclability, not operational efficiency alone.
02
Cat 11 Data Confidence
Consumer use (washing & drying) at 3,104 tCO₂e is estimated via Higg Index LCA benchmarks — lowest confidence tier. Actual magnitude depends on consumer market (EU vs India) and wash frequency. Flagged in disclosure.
03
Scope 2 — Clearest Near-Term Lever
Switching to renewable electricity / RECs eliminates ~5,500 tCO₂e under market-based method — the single highest-impact abatement action without capital investment in production processes.
04
Refrigerant GWP Risk
HFC-134a and HFC-410A leaks are small in kg terms but significant in tCO₂e due to GWPs of 1,430 and 2,088. Preventive maintenance programme = low-cost, high-credibility disclosure win.

## Slide 7
Praveen Gour | ESG Portfolio
Page 8
REDUCTION ROADMAP
Reduction Recommendations
Horizon 1
0–1 Year · Quick Wins
Renewable electricity / RECs
Scope 2
Impact: ~5,500 tCO₂e reduction
Refrigerant leak detection programme
Scope 1
Impact: Eliminate HFC losses; high credibility
Horizon 2
1–3 Years · Scaling
Supplier ESG engagement — primary data from top 10 cotton & polyester suppliers
Scope 3 Cat 1
Impact: Improves data quality; enables switching decisions
Modal shift: road → rail for inbound logistics
Scope 3 Cat 4
Impact: Road EF = 2.2× rail; 20% shift → ~30 tCO₂e
Horizon 3
3–5 Years · Transform
Product design for durability & recyclability
Scope 3 Cat 11/12
Impact: Structural; highest long-term impact
N₂O abatement: low-temp & enzyme-based dyeing
Scope 1
Impact: Process redesign; reduces GHG + energy intensity

## Slide 8
Praveen Gour | ESG Portfolio
Page 9
SKILLS DEMONSTRATED
Tools, Frameworks & Reporting Relevance
GHG Standard
GHG Protocol Corporate Accounting & Reporting Standard
EF Sources
CEA CO₂ Baseline 2023 · DEFRA 2023 · IPCC 2006 · EEIO US v1.1 · Higg Index
Calculation
Microsoft Excel — raw activity data, EF lookup, tCO₂e formula, scope aggregation, intensity ratios
Visualisation
Power BI — scope share donut, emissions by fuel type, total tCO₂e KPI card
Scope 3 Method
Activity-based (transport, travel, waste) · Spend-based EEIO (Cat 1) · LCA-based Higg Index (Cat 11)
Reporting Framework Relevance
BRSR
Principle 6 · Essential Indicators · Scope 1/2/3
GRI 305
305-1 (Direct) · 305-2 (Energy indirect) · 305-3 (Other indirect)
CDP C6
Emissions data · Scope 3 categories · Intensity metrics
CSRD ESRS E1
GHG emissions · Value chain · Decarbonisation targets